## Slide 1: ASTUTE
Smart Washing Machine
K.CHANDRAPRAKASH
N.SAI GANESH
V.CHANDRAKIRAN
R.SASHANK SHARMA

## Slide 2: ABSTRACT-
USUALLY IN HOSTELS WE HAVE A HUGE DEMAND FOR WASHING MACHINES.
IT IS BUSY, WE GO AWAY DISAPPOINTED,AGAIN WE COME AND OBSERVE THAT THE SAME THING REPEATS.WE SOLVED THIS PROBLEM UNTIL A LEVEL.
THROUGH OUR PROJECT,WHAT WE DO IS WHEN THE PERSON REQUESTS OUR WEBPAGE,HE WILL BE KNOWING STATE IN WHICH WASHING MACHINE IS.ANYONE CAN REQUEST THE WEBPAGE,SO HE OR SHE WILL BE ABLE TO KNOW IN WHAT STATE THE WASHING MACHINE IS AND CAN PLAN THEIR LAUNDRY.

## Slide 3: FULL DESCRIPTION
WE USED A CURRENT SENSOR SO THAT WE WOULD USE IT TO MEASURE THE CURRENT THAT THE WASHING MACHINE TAKES.
BECAUSE WE KNOW THAT AT DIFFERENT STATES THE POWER CONSUMED BY THE WASHING MACHINE IS DIFFERENT AND SO IS THE CURRENT.
WE THEN USED AN ARDUINO BOARD TO MONITOR THE CURRENT VALUE THAT HAVE BEEN MEASURED BY THE CURRENT SENSOR AND SIMULTANEOUSLY WE ALSO MONITORED THE WASHING MACHINE DISPLAY TO KNOW IN WHICH STATE THE WASHING MACHINE IS IN.
WE THEN OBSERVED THAT THE VALUES WERE IN SOME SORT OF A RANGE.IT MEANS THAT FOR IN ONE MODE THE CURRENT VALUES WERE IN SOME RANGE AND FOR ANOTHER MODE IT WAS IN THE ADJACENT (IN SOME CASES ) OR A DIFFERENT RANGE OF VALUES OF CURRENT.
THIS IS AN OVERALL VIEW ABOUT THE PROJECT TO GET A PICTURE OF WHAT IS EMBEDDED INSIDE AND THE PROCESS OF MEASURING AND EXECUTING ACCORDINGLY
IS EXPLAINED BRIEFLY IN THE NEXT SLIDES…….

## Slide 4: EXEMPLARY EXPLANATION
DURING OUR PROJECT ,WHEN WE WERE MEASURING THE VALUES,WE OBSERVED THAT THE CURRENT VALUES ARE IN THE FOLLOWING RANGES
→ FOR OFF OR STANDBY MODE IT IS LESS THAN 0.07 TO 0.12 (STANDBY MODE)
→ FOR WATER IN OR OUT MODE IT CAME AROUND 0.12 TO 0.17
→ FOR DRIER MODE IT CAME AROUND 1.4 TO 1.6
→ FOR WASHING MODE IT CAME AROUND 3.4 TO 3.7

## Slide 5: EXPLANATION
              → IN ARDUINO WE HAD CODED IN SUCH A WAY THAT IT SENDS
              0 0 FOR OFF OR STANDBY MODE
              0 1 FOR WATER IN OR OUT MODE
              1 0 FOR DRIER MODE
              1 1 FOR WASHING MODE
              THESE ARE HIGH (1) AND LOW (0) SIGNALS THROUGH DIGITAL PINS
              → IN THE RASPBERRY PI PART WHAT WE HAD DONE IS RECEIVED THE DATA(I.E; 0 1 ETC ) FROM ARDUINO AND DISPLAYED THE WEB PAGE ACCORDINGLY.

## Slide 6: EXPLANATION
            → UNFORTUNATELY WE HAD LOST MOST OF THE FILES(WEB PAGES PART) OF RASPBERRY PI PART BUT WE CAN GIVE A GLIMPSE OF IT HERE TO REPRODUCE IT.
            → WHAT WE HAD DONE IS TAKEN FOUR STATIC WEB PAGES AND USED JINJA2 IN WHICH WE CAN WRITE IF ELSE CONDITION FOR DISPLAYING A WEBPAGE.
            → SO WHAT WE HAD DONE IS WROTE A SIMPLE CONDITION THAT IF THE INPUT DATA IS 1 0 THEN DISPLAY DRIER MODE PAGE AND ACCORDINGLY FOR OTHER.
            → THANKS FOR THE ATTENTION.

## Slide 7: NOTE
                → THESE VALUES CAN CHANGE FROM TYPE OF MACHINE TO ANOTHER TYPE OF MACHINE.
                → THE CURRENT SENSOR WHICH YOU ARE USING, IN THIS CASE I USED ACS712-HALL EFFECT CURRENT SENSOR (20 AMP).
                → YOU CAN USE OTHER CURRENT SENSORS BUT YOU NEED TO NOTE DOWN THE VALUES FOR ONCE AND THEN CHANGE THE OTHER CODE ACCORDINGLY.

## Slide 8: THANK YOU